## Slide 1: Control Theory
Kevin Dekemele, Jasper Juchem, Michel De Roeck
Department of Electromechanical, Systems and Metal Engineering

## Slide 2: Content (9-12h, 13-14h)
Control – an overview
State space
  Model & linearization
  Stabilization
  Feedback & Linear Quadratic Control
  Observation & Kalman Filter
System dynamical properties: Stabilize around equilibrium & observe with disturbance, noise and limited information

## Slide 3: Content (14-17h)
Control Architectures
  Input-output models
  Control Algorithms
    LQR
    LQG
  MIMO control: decoupling
  Model Predictive control
Assuming stability & observation, how do we get where we want, given constraints, costs, …. ?

## Slide 4: Control: An overview

## Slide 5: System: levitation of a ball
Notes: Vandaag zullen we over de basisconcepten gaan in procesdynamica, het regeln of controleren van dergelijke processen. We gaan typisch dynamica caracteristen en verschillende regelstrategin voorstellen.
Om alles wat vatbaarder te maken hebben we een educatieve opstelling, die wordt gebruikt bij de burgerlijk ingenieurs als labo-opdracht voo het vak modelleren en regelen van dynamische systemen.
De bedoeling van deze opstelling is om de bal niet alleen stabiel te krijgen, maar dit ook op eender welke plaats. Op de bal werkt de zwaartekracht, en Via een luchtstroom opgewekt door een ventilator, een weerstandsrakcht (drag force). Simpelweg als de weerstandkracht de zwaartekracht perfect compenseert staat de bal stil. Maar op welke positie.
Ik heb in simple woorden uitgelegt hoe deze opstelling werkt, maar laten we dit systeem nu in een generieker kader gieten om dynamische systemen in het algemeen te bestuderen, het doel van de les.

## Slide 6: Ideal process
= Input fully determines output
Real process
Disturbance: ‘Input’ we have no control over,
Changes in assumed model
Sensor noise: Sensor never exact
Process
Model
Equilibrium
Hard to stabilize
Position difficult to choose
Process
Disturbance
Sensor noise
Notes: Allereerst, het process heeft een ingang, een parameter we volledige controle over hebben die de uitgang, hetgeen we willen aansturen . Hier is de ingang de snelheid van de ventilator en de uitgang de positie van de bal. Met deze blokken stellen we het oorzakelijk verband voor.
Zoals daarnet gezegd worden er krachten uitgeoefend op de bal, die met de tweede wet van netwon een differentiaalvergelijking geven. Typisch in de dynamica zijn er behoud of krachtwetten of balansen die het process mbv zulke vergelijking mdoelleren. De weerstandskracht is evenredig met het kwadraat van het snelheidsverschil.
Zoals gezegt moet de weerstandskracht de zwaarterkracht volledig compenseren zodat de bal niet beweegt. Bij elke Kleine afwijkijng echter, zal de versnelling van het balletje er voor zorgen dat het balletje ofwel blijft stijgen of dalen. Doordat we met onze ingang eigenlijk rechstreeks de tweede afgeleide aanpassen van de uitgang, wordt dit een integrerend proces genoemd, omdat we de versnelling twee keer moeten integreren.
NU is het niet zo dat alles wat onze uitgang doet volledig door onze aanpasbare ingang komt. Een verstoring of andere ingang die we niet helemaal in de hand hebben kan ook invloed hebben op de uitgang. Verder als we een sensor gebruiken, komt er vaak ruis bij.

## Slide 7: Feedback and control algoritmh
Sensor dynamics: Usually much faster than process (e.g. thermocouple)
Control algorithm: Algorithm to modify input based on measured value and option setpoint
Optimize speed, energy cost, stabilize, tracking (error=0)
Process
Controller
Sensor
Disturbance
Sensor noise
Notes: Om de positie van de bal naar een gewenste positie te brengen, gaan we gebruik maken van een sturing of regelalgorime.
Een regelalgoritme zal, zolang de gewenste positie niet bereikt is, de ingang bijsturen. Het verschil tussen gewenste waarde en gemeten waarde heet de fout.
We passen dus zelf niet niet meer de ingang aan, maar het algoritme doet dit.
Een gangbare, maar verre van optimale en die voor bais kan zorgen is een on/off regeling. Dit kennen we van de centrale verwarming, waar zolang de gewenste temperatuur niet bereijkt worden de verwarming aan gaat. Eenmaal bereikt gaat de verwarming uti. Typisch gaat de uitgang dat in een sorot band rond de wenswaarde liggen, met vaak veel energiegvebruik.

## Slide 8: Control algorithm
P: control as long as there is an error
I: control as long as a sum of error
D: control as long as there is a derivative of the error
Notes: In deze les gaan we doordachter om met controle. Een gekent algoritme is de PID waarde, die op basis van de fout, en de integral en afgeleide er. De P, of proportioneel is redelijk intuitief. Zolang de fout niet 0, blijf bijsturen. De D of differential zal bijsturen zolang de fout wijzigd. De I-actie of integrende actie de fout optellen (die positief of negatief kan zijn). Typisch zal dit er voor zorgen dat, als met een P regelaar er een fout blijft, deze wordt weggerelegld.

## Slide 9: Open vs CLOSD
Based on history or existing model, provide input
Based on measured output, provide input
Fuel rate model cruise control
Crane positioning

## Slide 10: Self driving
Vehicle dynamics
Tracking road
Disturbance road
Sensors & GPS
Decide fuel and steer angels based on this information

## Slide 11: Aerospace
Rocket dynamics
Stabilize and desired location
Side and main thrusters
https://users.ugent.be/~kdkemele
/rocket2018/

## Slide 12: HEATING
Heating room
Disturbance (window, sun)
Lowering energy use
Energy balance

## Slide 13: predator Prey/ Infection
Many prey -> many predators
Too much compitino and less food -> less predators
Less predators -> more prey
Compition model
What happens with disturbance?

## Slide 14: (Bio) Chemical reactor
Balance Removed heat = generated heat
‘Instable’ points might provide best generation of substance B
Feedback

## Slide 15: Steel factory

## Slide 16: Continuous caster
Level of steel control
Determines quality
Two cascades systems
  Stopper (fast)
  Level of caster (slow)

## Slide 17: State Space

## Slide 18: Matrices and vectors
Matrix Vectors
Determinant
-

## Slide 19: Eigenvectors and values
Matrix maps column vector into another one with transformation:
Rotation matrix:
Eigenvector maps to itself with a factor (= eigenvalue)

## Slide 20: Eigenvectors and values: steps
Determine eigenvalues
Then compute eigenvectors

## Slide 21: Eigenvector and values: Diagonalization
and

## Slide 22: Basic Mathematics: Taylor series
Change of coordinates

## Slide 23: Models
Let of Linear Time Invariant first order ODEs (LTI systems)
State vector
Input vector (How to intervene in dynamics)
  Disturbances (inputs, but not from us)
Output vector (What we can measure)
: System Matrix
: Input Matrix
: Output Matrix

## Slide 24: Models: Discrete time
Set of linear Difference equations:
Used in Model Predictive control
Conversion Continuous to discrete time:

## Slide 25: Linearization
Taylor series around operational or equilibrium point ( = 0),

## Slide 26: Pendulum

## Slide 27: Pendulum on cart = Crane
b = 1 (up)
b = -1 (down)

## Slide 28: Levitation of ball
We only measure position

## Slide 29: Competition model
: Rabbit population
: Sheep population

## Slide 30: Eigenvalues & Eigenvectors
Autonomous system:
Solution ???
Eigenvalues/vectots of , and
Eigenmodes

## Slide 31: Eigenvalues & Eigenvectors
Solution
What types of time responses are there??

## Slide 32: Eigenvalues & Stability
Oscillations
Process
Unstable
Figures:
https://odysc.ugent.be

## Slide 33: Eigenvalues & Stability
Oscillations
Process
Unstable

## Slide 34: Eigenvalues, Eigenvectors & Stability
Eigenvalues in dynamical system meaning:
  Stability & Speed
  Response is exponential of eigenvalues, weighted by eigenvectors
  (if x(0) is an eigenvector, you stay on this vector)

## Slide 35: Pendulum

## Slide 36: Pendulum on cart = Crane
SHOW IN PYTHON

## Slide 37: Levitation of ball

## Slide 38: Competition model
Intervene by adding/removing sheep or rabbits
=FEEDBACK

## Slide 39: ‘Forced’ response
(convolution integral)
Forced response
  Transient determined by eigenvalues & vectors
  Steady state part, weighted version of u
Python example: Intro to control toolbox
Response to frequency: gain and phase
See later (Input/Output & Laplace)

## Slide 40: Example forced: Suspension
Parameter | Value
Sprung mass | 332 kg
Unsprung mass | 100 kg
Suspension spring | 48000 N/m
Tire spring | 200 000 N/m
Suspension damper | 1000 Nm/s
Parameter | Value
 | 332 kg
 | 100 kg
 | 48000 N/m
 | 200 000 N/m
 | 1000 Nm/s
Lajqi, S., & Pehan, S. (2012).
Designs and optimizations of active and semi-active non-linear suspension systems for a terrain vehicle.
Strojniški vestnik-Journal of Mechanical Engineering, 58(12), 732-743.

## Slide 41: State feedback
Eigenvalues determine stability, speed & oscillations
Can we choose such that we can change the eigenvalues? STATE FEEDBACK =
Requires FULL state knowledge

## Slide 42: Controllability
Controllability matrix
If rank matrix is , system is controllable
  Arbitrary eigenvalue placement through state feedback
  Reachability: any state can be reached in finite time, for some
Python inverted pendulum

## Slide 43: Pole Placement
Eigenvalue on the real axis
As negative as possible?
Python command ‘Place’
Inverted pendulum example

## Slide 44: Pole Placement
Why is there a balance?
Nonlinear might not be actually stable??
Stabilisation Speed
Control Effort
Weighted cost
Constraints?

## Slide 45: Designing feedback: Linear Quadratic control
Controllabilty means a can stabilize and change eigenvalues. How to choose ?
Weight optimization between fast stabilization and input cost
(“Energy”)

## Slide 46: Designing feedback: Linear Quadratic control
Optimal
Where is the solution of a ‘stationary Ricatti’ equation:
Inverted pendulum example

## Slide 47: Designing feedback: LQR reference
We want
and
Stable if =
So same optimization holds, different meaning input cost

## Slide 48: State estimation
Until now: Knowledge full state
Output equation!
Not all state can be measured because
of limited sensors, measurement locations

## Slide 49: Observability
Observability matrix
If rank matrix is , system is observable
  any state can be estimated from in finite time, for some
  Similar like controllability second meaning!

## Slide 50: Observer
Estimated dynamics based on
Estimation error dynamics:
Pole placement/stabilisation! But how to choose ?

## Slide 51: Kalman Filter
)
, )
)=)=0 )=)=
Observer gain optimization under system and measurement noise
Optimal
Where is the solution of a ‘stationary Ricatti’ equation:
Large input noise: Trust measurement, more gain
Large output noise: Trust estimation, less gain
Matlab example

## Slide 52: Estimation & control

## Slide 53: Example: Inverted pendululm
Robustness? Does control still work if model estimation wrong?
https://www.youtube.com/watch?v=D3bblng-Kcc

## Slide 54: Advanced topics?
Nonlinear Kalman
Reduced observer (not all states)
Stopgap: Linear Parameter varying:
Advanced libraries usually MATLAB & SIMULINK

## Slide 55: References
Linear Systems (Course Ghent University, Gert De Cooman)
Control System Design and Management (Course University of Newcastle, Julio Braslavsky)
Brunton, S. L., & Kutz, J. N. (2022). Data-driven science and engineering: Machine learning, dynamical systems, and control. Cambridge University Press.
Chevalier, A., Dekemele, K., Juchem, J., & Loccufier, M. (2021). Student feedback on educational innovation in control engineering: active learning in practice. IEEE Transactions on Education, 64(4), 432-437.
Strogatz, S. H. (2018). Nonlinear dynamics and chaos: with applications to physics, biology, chemistry, and engineering. CRC press.

## Slide 56: Input-output models

## Slide 57: Laplace transform
The Laplace transform:
In short: to go from differential - to algebraic equations

## Slide 58: From state-space to input-output models
We are interested in the relationship between the inputs and (measurable) outputs (i.e. not necessarily all the states)
Consider a linear system
Laplace transform:
Often:

## Slide 59: Mimo control

## Slide 60: Beam rolling: example
Goal: track static reference thickness
Notes: Explain process
Beam deformation
Two direction apply
Control rolling force
Also uncontrolled variables: gap thickness
Input is a force
Focus on robust control (i.e. against disturbances)
Advanced control techniques developed throughout the example (illustration)
Goal is to develop some feeling with these techniques, what they mean, how they apply, challenges

## Slide 61: Beam rolling: Process (x-direction)
: controlled input
: eccentricity (disturbance)
: input thickness (disturbance)
gap thickness (not measurable)
rolling force (measurable)
Dynamics
Notes: Start simple: neglect on direction

## Slide 62: Basic control: PID
Easy tuning rules:
  Oscillation test results in
  E.g. Ziegler-Nichols:
More involved tuning based on some quality labels:
  Overshoot
  Settling time

## Slide 63: Beam rolling: LQR control (x-direction)
Define cost function:
Wherein
Result: control law
But…
Python exercise
Notes: See earlier reference not important for optimal solution

## Slide 64: LQG control
Boils down to: Kalman + LQR
LQR, using an estimate of the full state:
Kalman to estimate the state
u: plant input
y: plant output
w: input disturbance
v: output disturbance

## Slide 65: Beam rolling: LQG control (x-direction)
: controlled input
: disturbance (eccentricity)
: disturbance (input thickness)
gap thickness (not measurable)
rolling force (measurable)
Python implementation

## Slide 66: Beam rolling: x & y direction
Interactions exist:
  Example: Poisson coefficient
Complicating control:
  Input influences
  Input influences
  Cross coupling
How to deal with this?

## Slide 67: Decoupled control
Coupling between and exist
How to deal with this?
  Ignore coupling (Decentralised Control):
    LQR or LQG for separated models suboptimal solution
    ‘What is good for one might be bad for the other’
  Take coupling into account (Centralised Control):
    Difficult to comprehend
    LQR or LQG: complicated model and often suboptimal
  Decouple in control scheme!
To what degree do and interact?
  Relative Gain Array (RGA)

## Slide 68: Decoupled control: Relative Gain Array (1)
Consider the input-output model:
Gain from to (all other loops open):
Gain from to (all other loops closed):
Relative gain:
With:

## Slide 69: Decoupled control: Relative Gain Array (2)
Apply a step input keeping constant () and measure the output change
Apply a step input keeping constant () (i.e. keeping all other loops closed and measure the output change

## Slide 70: Beam Rolling: decoupling control (1)
Input-output model:
With:
&

## Slide 71: Beam Rolling: decoupling control (2)
such that inputs and outputs are decoupled i.e. no interaction between and and and
We aim at static decoupling:
? Exercise

## Slide 72: Beam Rolling: decoupling control (3)
Consider the new input-output model:
Wherein:
We aim at static decoupling:
Goal: find for such that and are decoupled

## Slide 73: Beam Rolling: Decentralised Control
Ignore interactions altogether
  Design an LQR based on a model for the x-direction
  Design an LQR based on a model for the y-direction
  Apply inputs and as such
Justification:
  The RGA method shows low degrees of interaction
  Note: coupling & w.r.t. are not considered
RGA-matrix

## Slide 74: Beam Rolling: Centralised Control
Model the plant completely (including interactions)
  Design one LQR based on the full model
  Apply inputs and as such (generated by the same LQR)
Justification:
  The RGA method might show high degrees of interaction

## Slide 75: Model Predictive Control (MPC):
Unaddressed topics so far:
  Constraint equations
  Nonlinear models
  Dead time
  Dealing measured disturbances
MPC

## Slide 76
MPC :
Feedback control for MIMO systems
Input based on real-time optimisation
Optimisation based on current state and predicted future output
MPC:
Current time t

## Slide 77: MPC
Based on a model (state-space):
And a well-defined cost function:
Taking into account some constraints:
Minimisation of the cost function, based on the predicted output (and therefore the predicted error) results in over the prediction horizon
Only applied
Possibly:

## Slide 78: Process: Industrial polymerisation reactor
Ref: https://www.do-mpc.com/en/latest/example_gallery/industrial_poly.html
Input

## Slide 79: Model through conservation
Parameter uncertainty

## Slide 80: Constraints

## Slide 81: Objective
Produce as fast as possible
Smooth control performance: penalty on input changes